## Slide 1: Computer Architecture A Quantitative Approach, Fifth Edition
Chapter 2
Memory Hierarchy Design

## Slide 2: Introduction

Programmers want unlimited amounts of memory with low latency
Fast memory technology is more expensive per bit than slower memory
Solution: organize memory system into a hierarchy



Entire addressable memory space available in largest, slowest memory
Incrementally smaller and faster memories, each containing a subset of the memory below it, proceed in steps up toward the processor


Temporal and spatial locality insures that nearly all references can be found in smaller memories

Gives the allusion of a large, fast memory being presented to the processor
Introduction

## Slide 3: Memory Hierarchy
Introduction

## Slide 4: Memory Performance Gap
Introduction

## Slide 5: Memory Hierarchy Design

Memory hierarchy design becomes more crucial with recent multi-core processors:
Aggregate peak bandwidth grows with # cores:

Intel Core i7 can generate two references per core per clock Four cores and 3.2 GHz clock


25.6 billion 64-bit data references/second +
12.8 billion 128-bit instruction references
= 409.6 GB/s!

DRAM bandwidth is only 6% of this (25 GB/s) Requires:



Multi-port, pipelined caches Two levels of cache per core Shared third-level cache on chip
Introduction

## Slide 6: Performance and Power

High-end microprocessors have >10 MB on-chip cache
Consumes large amount of area and power budget
Introduction

## Slide 7: Memory Hierarchy Basics

When a word is not found in the cache, a miss
occurs:


Fetch word from lower level in hierarchy, requiring a higher latency reference
Lower level may be another cache or the main memory
Also fetch the other words contained within the block
Takes advantage of spatial locality
Place block into cache in any location within its set, determined by address
block address MOD number of sets

Introduction

## Slide 8: Memory Hierarchy Basics
n sets => n-way set associative
  Direct-mapped cache => one block per set
  Fully associative => one set

Writing to cache: two strategies
Write-through
  Immediately update lower levels of hierarchy
Write-back

Only update lower levels of hierarchy when an updated block is replaced
Both strategies use write buffer to make writes asynchronous

Introduction

## Slide 9: Memory Hierarchy Basics
Miss rate
  Fraction of cache access that result in a miss
Causes of misses
  Compulsory
    First reference to a block
  Capacity
    Blocks discarded and later retrieved
  Conflict
    Program makes repeated references to multiple addresses from different blocks that map to the same location in the cache
Introduction

## Slide 10: Memory Hierarchy Basics

Note that speculative and multithreaded processors may execute other instructions during a miss
Reduces performance impact of misses
Introduction

## Slide 11: Memory Hierarchy Basics
Six basic cache optimizations:

Larger block size

Reduces compulsory misses
Increases capacity and conflict misses, increases miss penalty


Larger total cache capacity to reduce miss rate

Increases hit time, increases power consumption

Higher associativity

Reduces conflict misses
Increases hit time, increases power consumption


Higher number of cache levels

Reduces overall memory access time

Giving priority to read misses over writes

Reduces miss penalty

Avoiding address translation in cache indexing

Reduces hit time
Introduction

## Slide 12: Ten Advanced Optimizations
Small and simple first level caches
  Critical timing path:


addressing tag memory, then comparing tags, then selecting correct set

Direct-mapped caches can overlap tag compare and transmission of data
Lower associativity reduces power because fewer cache lines are accessed

Advanced Optimizations

## Slide 13: L1 Size and Associativity
Access time vs. size and associativity
Advanced Optimizations

## Slide 14: L1 Size and Associativity
Energy per read vs. size and associativity
Advanced Optimizations

## Slide 15: Way Prediction

To improve hit time, predict the way to pre-set mux

Mis-prediction gives longer hit time Prediction accuracy


> 90% for two-way
> 80% for four-way
I-cache has better accuracy than D-cache
First used on MIPS R10000 in mid-90s
Used on ARM Cortex-A8
Extend to predict block as well

“Way selection”
Increases mis-prediction penalty
Advanced Optimizations

## Slide 16: Pipelining Cache
Pipeline cache access to improve bandwidth
  Examples:


Pentium: 1 cycle
Pentium Pro – Pentium III: 2 cycles Pentium 4 – Core i7: 4 cycles

Increases branch mis-prediction penalty Makes it easier to increase associativity

Advanced Optimizations

## Slide 17: Nonblocking Caches

Allow hits before previous misses complete

“Hit under miss”
“Hit under multiple miss”


L2 must support this
In general, processors can hide L1 miss penalty but not L2 miss penalty

Advanced Optimizations

## Slide 18: Multibanked Caches

Organize cache as independent banks to support simultaneous access

ARM Cortex-A8 supports 1-4 banks for L2
Intel i7 supports 4 banks for L1 and 8 banks for L2

Interleave banks according to block address
Advanced Optimizations

## Slide 19: Critical Word First, Early Restart
Critical word first
  Request missed word from memory first
  Send it to the processor as soon as it arrives

Early restart
Request words in normal order
Send missed work to the processor as soon as it arrives

Effectiveness of these strategies depends on block size and likelihood of another access to the portion of the block that has not yet been fetched
Advanced Optimizations

## Slide 20: Merging Write Buffer

When storing to a block that is already pending in the write buffer, update write buffer
Reduces stalls due to full write buffer Do not apply to I/O addresses


Advanced Optimizations
No write buffering
Write buffering

## Slide 21: Compiler Optimizations
Loop Interchange
  Swap nested loops to access memory in sequential order
Blocking

Instead of accessing entire rows or columns, subdivide matrices into blocks
Requires more memory accesses but improves locality of accesses
Advanced Optimizations

## Slide 22: Hardware Prefetching

Fetch two blocks on miss (include next sequential block)
Advanced Optimizations
Pentium 4 Pre-fetching

## Slide 23: Compiler Prefetching

Insert prefetch instructions before data is needed
Non-faulting: prefetch doesn’t cause exceptions
Register prefetch
  Loads data into register
Cache prefetch
  Loads data into cache

Combine with loop unrolling and software pipelining
Advanced Optimizations

## Slide 24: Summary
Advanced Optimizations

## Slide 25: Memory Technology
Performance metrics


Latency is concern of cache
Bandwidth is concern of multiprocessors and I/O Access time

Time between read request and when desired word arrives
Cycle time

Minimum time between unrelated requests to memory
DRAM used for main memory, SRAM used for cache

Memory Technology

## Slide 26: Memory Technology
SRAM
  Requires low power to retain bit
  Requires 6 transistors/bit

DRAM

Must be re-written after being read Must also be periodically refeshed
Every ~ 8 ms
Each row can be refreshed simultaneously

One transistor/bit
Address lines are multiplexed:


Upper half of address: row access strobe (RAS) Lower half of address: column access strobe (CAS)
Memory Technology

## Slide 27: Memory Technology
Amdahl:

Memory capacity should grow linearly with processor speed
Unfortunately, memory capacity and speed has not kept pace with processors


Some optimizations:

Multiple accesses to same row Synchronous DRAM


Added clock to DRAM interface Burst mode with critical word first


Wider interfaces Double data rate (DDR)
Multiple banks on each DRAM device


Memory Technology

## Slide 28: Memory Optimizations
Memory Technology

## Slide 29: Memory Optimizations
Memory Technology

## Slide 30: Memory Optimizations
DDR:
  DDR2

Lower power (2.5 V -> 1.8 V)
Higher clock rates (266 MHz, 333 MHz, 400 MHz)

DDR3

1.5 V
800 MHz

DDR4

1-1.2 V
1600 MHz

GDDR5 is graphics memory based on DDR3
Memory Technology

## Slide 31: Memory Optimizations
Graphics memory:
  Achieve 2-5 X bandwidth per DRAM vs. DDR3

Wider interfaces (32 vs. 16 bit) Higher clock rate

Possible because they are attached via soldering instead of socketted DIMM modules

Reducing power in SDRAMs:

Lower voltage
Low power mode (ignores clock, continues to refresh)
Memory Technology

## Slide 32: Memory Power Consumption
Memory Technology

## Slide 33: Flash Memory

Type of EEPROM
Must be erased (in blocks) before being overwritten
Non volatile
Limited number of write cycles
Cheaper than SDRAM, more expensive than disk
Slower than SRAM, faster than disk





Memory Technology

## Slide 34: Memory Dependability

Memory is susceptible to cosmic rays
Soft errors: dynamic errors


Detected and fixed by error correcting codes (ECC)
Hard errors: permanent errors

Use sparse rows to replace defective rows

Chipkill: a RAID-like error recovery technique
Memory Technology

## Slide 35: Virtual Memory
Protection via virtual memory
  Keeps processes in their own memory space
Role of architecture:




Provide user mode and supervisor mode Protect certain aspects of CPU state
Provide mechanisms for switching between user mode and supervisor mode
Provide mechanisms to limit memory accesses Provide TLB to translate addresses
Virtual Memory and Virtual Machines

## Slide 36: Virtual Machines

Supports isolation and security
Sharing a computer among many unrelated users
Enabled by raw speed of processors, making the overhead more acceptable



Allows different ISAs and operating systems to be presented to user programs

“System Virtual Machines”
SVM software is called “virtual machine monitor” or “hypervisor”
Individual virtual machines run under the monitor are called “guest VMs”


Virtual Memory and Virtual Machines

## Slide 37: Impact of VMs on Virtual Memory

Each guest OS maintains its own set of page tables

VMM adds a level of memory between physical and virtual memory called “real memory”
VMM maintains shadow page table that maps guest virtual addresses to physical addresses

Requires VMM to detect guest’s changes to its own page table
Occurs naturally if accessing the page table pointer is a privileged operation
Virtual Memory and Virtual Machines